## Slide 1: Back-end Timing Models
Core Models
Interconnection Network
Memory System
  Coherence Cache Hierarchy
  DRAM Controller

## Slide 2: Core Models
Zesto – cycle-level x86 processor model
SPX – a light pipe-lined model
SimpleProc – a 1-IPC model

## Slide 3: Zesto* Overview
Consists of an oracle and a detailed pipeline
Oracle is an “execution-at-fetch” functional simulator; fetched instructions are first passed to oracle
Pipeline has 5 stages
Very detailed; slow (10’s of KIPS)
Ported to Manifold as a component
*G. Loh, etc., “Zesto: a cycle-level simulator for highly detailed microarchitecture exploration,” International Symposium on Performance Analysis of Software and Systems (ISPASS), pp53-64, 2009
Oracle
(functional)
Detailed pipeline model
(superscalar / OOO pipeline)
cache
x86 instructions6
recovery info
memory requests
and replies

## Slide 4: Zesto
X86 based timing model derived from Zesto cycle-level simulator
  IA 32 support

## Slide 5: Zesto Interface
Front-end interfaces
Cache request
Event handler (for cache response)
Clocked function
Multiple instances with different front-end interfaces

## Slide 6: Zesto Interface
ZestoCacheReq
event handler for cache response
class core_t {
public:
...
void cache_response_handler(int, ZestoCacheReq*);
...
};

## Slide 7: Zesto Interface
Clocked function
  must be registered with a clock
  Zesto does not register this function, so it must be registered in the simulator program.
void core_t :: tick()
{
//get the pipeline going
commit->step();
exec->LDST_exec();
...
alloc->step();
decode->step();
fetch->step();
...
}

## Slide 8: Simplified Pipeline eXecution (SPX) <A simpler, lighter core model for out-of-order and in-order pipelines>

## Slide 9: SPX
SPX is an abbreviated core model that support both out-of-order and in-order executions.
Purpose: Detail vs. Speed
  For less core-sensitive simulations (i.e., memory/network traffic analysis), detailed core implementation may be unnecessary.
  Physics simulations need longer observation time (in real seconds) than typical architectural simulations
    e.g., temperature doesn’t change much for several hundreds million clock cycles (or several hundred milliseconds) of simulation.
The SPX model provides enough details to model out-of-order and in-order executions, and other optional behaviors are all abbreviated (e.g., predictions)
The SPX requires Qsim Library for detailed instruction information.
  Queue model is not currently supported.
  SPX uses direct Qsim callback functions.

## Slide 10: Modeled Components in SPX
InstQ: A queue that fetches the instructions from Qsim.
RF: Register file that tracks only dependency; behaves more like RAT.
  Dependency for general register files and flags are maintained.
RS: Dependency status tracker.
  It does not have an actual table like scoreboard.
  When an instruction is ready (cleared from dependency), it is put in the ReadyQ.
  In-order execution is modeled with 1-entry RS.
EX (FU): Multi-ported execution units.
  Each FU is defined with latency and issue rate.
ROB: Re-order buffer for out-of-order execution
  An instruction can be broken into multiple sub-instructions (e.g., u-ops), and ROB commits the instruction when all sub-instructions are completed.
LDQ/STQ: Load and store queues
  These queues check memory dependency between ST/LD instructions.

## Slide 11: Out-of-order Pipeline
InstQ
Qsim Lib
Callbacks
Translation to SPX instruction
ROB
RS
LDQ
STQ
Allocate if Available
RF
Allocate if Available
Allocate if LD
And Available
Allocate if ST
And Available
Resolve Dependency
Reg. Dep.
Status
EX
FU
FU
FU
FU Port Binding
Mem. Dep.
CheckWhen Allocate
Schedule
Schedule When Commit
Cache Req. After EX
Cache Req. After Commit
Update
Store Fwd
Update
Cache Resp.
Update
Writeback

## Slide 12: In-order Pipeline
InstQ
Qsim Lib
Callbacks
Translation to SPX instruction
threadQ
LDQ
STQ
RF
Allocate if Available
Allocate if LD
And Available
Allocate if ST
And Available
Resolve Dependency
Reg. Dep.
Status
EX
FU
FU
FU Port Binding
Mem. Dep.
CheckWhen Allocate
Schedule
Cache Req. After EX
Cache Req. After EX
Writeback
Store Fwd
Update
Cache Resp.
Update
Schedule

## Slide 13: SPX Interface
Front-end
Cache request
Event handler (for cache response)
Clocked function

## Slide 14: SPX Interface
cache_reqest_t
event handler for cache response
class spx_core_t {
public:
...
void handle_cache_response(int, cache_reqest_t*);
...
};
clocked function
  must be registered with a clock
  SPX does not register this function, so it must be registered in the simulator program.
void spx_core_t :: tick()
{
...
}

## Slide 15: SimpleProc
1-IPC: in general one instruction is executed every cycle
MSHR limits number of outstanding cache requests

## Slide 16: SimpleProc Interface
Front-end
Cache request
Event handler (for cache response)
Clocked function

## Slide 17: SimpleProc Interface
CacheReq
event handler for cache response
class SimpleProcessor {
public:
...
void handle_cache_response(int, CacheReq*);
...
};
clocked function
  must be registered with a clock
  SimpleProc does not register this function, so it must be registered in the simulator program.
void SimpleProcessor :: tick()
{
...
}

## Slide 18: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators