## Slide 1: Building and Running Parallel Simulations
Instantiate Components
Connect Components
Register Clocks
Simulation Functions
Initialization
Configuration parameters
From Manifold Library
Inputs (trace, QSIM, etc.)
Instantiate Links
Set Timing Behavior
Time stepped vs. discrete event
Set Duration, Cleanup, etc.

## Slide 2: Building and Running Parallel Simulations
Kernel Interface
Simulator Construction
Logs and Statistics
Demos

## Slide 3: Kernel Interface
Component functions
  create component
    component can have 0-4 constructor arguments
    template allows constructor parameters to be any type
    returns unique integer ID
Component::Create<qsimclient_core_t>(lp, node_id, m_conf, cpuid, proc_settings);
//component-decl.h
template <typename T>
static CompId_t Create(LpId_t, CompName name=CompName(“none”));
...
template <typename T, typename T1, typename T2, typename T3, typename T4>
static CompId_t Create(LpId_t, const T1&, const T2&, const T3&, const T4&, CompName name=CompName(“none”));

## Slide 4: Kernel Interface
  Connect components
    one-way connection
    two-way connection
//manifold-decl.h
template<typename T, typename T2>
static void Connect(CompId_t srcComp, int srcIdx, CompId_t dstComp, int dstIdx, void (T::*handler)(int, T2), Ticks_t latency);
//manifold-decl.h
template<typename T, typename T2, typename U, typename U2>
static void Connect(CompId_t comp1, int idx1, void (T::handler1)(int, T2), CompId_t comp2, int idx2, void(U::*handler2)(int, U2), Clock& clk1, Clock& clk2, Ticks_t latency1, Ticks_t latency2);
Source
component
Destination
component
srcIdx
dstIdx

## Slide 5: Kernel Interface
Clock functions: constructor, Register()
//clock.h
Clock(double freq);
template<typename O>
static tickObjBase* Register(Clock& clk, O* obj, void (O::*rising)(void)
void (O::*falling)(void));
simulation functions
//manifold-decl.h
static void Init(int argc, char**argv, SchedulerType=TICKED,
SyncAlg::SyncAlgType_t syncAlg=SyncAlg::SA_CMB_OPT_TICK,
Lookahead::LookaheadType_t la=Lookahead::LA_GLOBAL);
static void Finalize();
static void StopAt(Ticks_t stop);
static void Run();

## Slide 6: Simulator Construction
Steps for building a simulation program
  Call Manifold::Init()
  Build system model: Clock(); Create(), Connect(), Register()
  Set simulation stop time: StopAt()
  Call Manifold::Run()
  Call Manifold::Finalize()
  Print out statistics: print_stats()

## Slide 7: Logs and Statistics
Each component collects its own statistics
A convention for printing stats is:
  void print_stats(std::ostream&);

## Slide 8: Example Simulators
Simulator 1:
  For demo purposes only
  Builds a 2-core system
    2 Zesto cores
    MCP cache
    Iris(2x2 torus)
    CaffDRAM
  Runs sequential or parallel (3 LPs) simulation
Simulator 2:
  Part of software distribution
  3 programs: work with Qsim server, Qsim lib, and traces, respectively
  Core model can be replaced with one-line change to configure file

## Slide 9: Sample Results: Setup
16, 32, 64-core CMP models
2, 4, 8 memory controllers, respectively
5x4, 6x6, 9x8 torus, respectively
Host: Linux cluster; each node has 2 Intel Xeon X5670 6-core CPUs with 24 h/w threads
13, 22, 40 h/w threads used by the simulator on 1, 2, 3 nodes, respectively
200 Million simulated cycles in region of interest (ROI)
  Saved boot state and fast forward to ROI

## Slide 10: Sample Results: Simulation Time in Minutes
 | 16-core |  | 32-core |  | 64-core | 
 | Seq. | Para. | Seq. | Para. | Seq. | Para.
dedup | 1095.7 | 251.4 (4.4X) | 2134.8 | 301.3 (7.1X) | 2322.9 | 345.3 (6.7X)
facesim | 1259.3 | 234.9 (5.4X) | 2614.2 | 303.6 (8.6X) | 3170.2 | 342.3 (9.3X)
ferret | 1124.8 | 227.8 (4.9X) | 1777.9 | 255.6 (7.0X) | 2534.3 | 331.3 (7.6X)
freqmine | 1203.3 | 218.0 (5.5X) | 1635.6 | 245.6 (6.7X) | 2718.9 | 337.3 (8.1X)
stream | 1183.8 | 222.7 (5.3X) | 1710.6 | 244.3 (7.0X) | 4796.4 | 396.2 (12.1X)
vips | 1167.0 | 227.3 (5.1X) | 1716.3 | 257.2 (6.7X) | 2564.6 | 337.9 (7.6X)
barnes | 1039.9 | 224.3 (4.6X) | 1693.0 | 283.3 (6.0X) | 3791.8 | 341.4 (11.1X)
cholesky | 1182.4 | 227.2 (5.2X) | 1600.3 | 245.7 (6.5X) | 4278.3 | 402.1 (10.6X)
fmm | 1146.3 | 229.6 (5.0X) | 1689.8 | 253.6 (6.7X) | 5037.2 | 416.1 (12.1X)
lu | 871.2 | 156.4 (5.6X) | 1475.8 | 204.6 (7.2X) | 4540.3 | 402.7 (11.3X)
radiosity | 1022.3 | 228.8 (4.5X) | 1567.5 | 250.4 (6.3X) | 2813.5 | 350.3 (8.0X)
water | 671.5 | 158.4 (4.2X) | 1397.3 | 236.7 (5.9X) | 2560.1 | 356.3 (7.2X)

## Slide 11: Sample Results: Simulation in KIPS
 | 16-core |  | 32-core |  | 64-core | 
 | Seq. | Para. | Seq. | Para. | Seq. | Para.
dedup | 49.28 | 211.98 | 48.56 | 340.61 | 16.88 | 136.82
facesim | 58.66 | 316.42 | 47.90 | 401.72 | 30.01 | 278.94
ferret | 57.77 | 284.81 | 35.41 | 239.59 | 18.10 | 139.54
freqmine | 57.15 | 314.99 | 37.01 | 248.60 | 19.37 | 140.18
stream | 58.77 | 314.34 | 36.73 | 260.04 | 41.42 | 419.77
vips | 58.03 | 298.09 | 34.92 | 236.06 | 18.02 | 131.02
barnes | 30.66 | 151.32 | 32.62 | 168.74 | 39.61 | 219.63
cholesky | 57.95 | 301.47 | 38.87 | 254.54 | 45.68 | 491.46
fmm | 51.01 | 252.46 | 37.90 | 255.86 | 40.94 | 525.51
lu | 50.93 | 155.74 | 39.78 | 119.46 | 46.23 | 485.04
radiosity | 50.87 | 206.96 | 53.15 | 229.02 | 36.29 | 268.70
water | 27.86 | 95.81 | 29.85 | 132.22 | 25.72 | 179.88
Mean | 50.75 | 242.03 | 39.39 | 240.54 | 31.52 | 284.71
Median | 54.08 | 268.63 | 37.45 | 244.10 | 33.15 | 244.16

## Slide 12: Sample Results: KIPS per Hardware Thread
 | 16-core |  | 32-core |  | 64-core | 
 | Seq. | Para. | Seq. | Para. | Seq. | Para.
dedup | 49.28 | 16.31 | 48.56 | 15.48 | 16.88 | 3.42
facesim | 58.66 | 24.34 | 47.90 | 18.26 | 30.01 | 6.97
ferret | 57.77 | 21.91 | 35.41 | 10.89 | 18.10 | 3.49
freqmine | 57.15 | 24.23 | 37.01 | 11.30 | 19.37 | 3.50
stream | 58.77 | 24.18 | 36.73 | 11.82 | 41.42 | 10.49
vips | 58.03 | 22.93 | 34.92 | 10.73 | 18.02 | 3.28
barnes | 30.66 | 11.64 | 32.62 | 7.67 | 39.61 | 5.49
cholesky | 57.95 | 23.19 | 38.87 | 11.57 | 45.68 | 12.29
fmm | 51.01 | 19.42 | 37.90 | 11.63 | 40.94 | 13.14
lu | 50.93 | 11.98 | 39.78 | 5.43 | 46.23 | 12.13
radiosity | 50.87 | 15.92 | 53.15 | 10.41 | 36.29 | 6.72
water | 27.86 | 7.37 | 29.85 | 6.01 | 25.72 | 4.50
Mean | 50.75 | 18.62 | 39.39 | 10.93 | 31.52 | 7.12
Median | 54.08 | 20.66 | 37.45 | 11.09 | 33.15 | 6.10

## Slide 13: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators