## Slide 1
Energy Introspector: Integration of Physical Models

## Slide 2: Architecture-Physics Co-Simulation
Monitored Physics (Power, Temperature, etc.)
Architecture Simulations ➔ Physical phenomena
Physical Phenomena ➔ Control Algorithms
Control Algorithms ➔ Architectural Executions
Microarchitectural Simulation
(Functional Models)
Physical Phenomena
(Power)
(Temperature)
Physical Interactions
(Noise)
(Delay)
(Reliability)
…
Controller
Clock Freq.
Voltage, Clock Freq.

## Slide 3: Introduction to Energy Introspector
Energy Introspector (EI) is a simulation framework to facilitate the (selective) uses of different models and capture the interactions among microprocessor physics models.
Power Model Library
Reliability Model Library
Thermal Model Library
Coordinated Multi-Physics Interface
USER INTERFACE
compute_power();
compute_temperature();
INTERACTIONS
Model Library Wrappers
Microarchitecture
Description & Statistics
Available at www.manifold.gatech.edu
…

## Slide 4: Multi-Physics / Multi-Model Modeling
Different physical properties are modeled with different modeling tools.
Need to be able to easily integrate new models as they become available
  Costly when tightly integrated into microarchitecture simulation models
Power Modeling Tools
Thermal Modeling Tools
Reliability Modeling Tools
Delay Modeling Tools
McPAT (Cacti),
Orion (DSENT),
DRAMsim,
…
HotSpot,
3D-ICE,
TSI,
…
NBTI,
TDDB,
Electro-migration,
…
PDN,
Temperature Inversion,
…

## Slide 5: Physical Interaction Interface
Goals:
  Coordinated Modeling: The interface supports the modeling of different physical phenomena in the same domain of analysis by capturing their interactions; vs. trace-driven offline analysis
  Standardization: Different tools are integrated in the compatible way.
    Data definition is required for common, shared data.
    Different tools of the same data type can used in the identical way.
  Configurable Interface: Due to the integration of different tools, there must be a method to represent the different levels of processor components.
    Package | Floor-planning | Architecture/Circuit-level Blocks
  Data Synchronization: Data are shared between multiple tools.
  User Interface: User API is provided to trigger the calculation.
    The interface handles the data synchronization and interactions.
We introduce the Energy Introspector (EI) interface.

## Slide 6: COORDINATED MODELING: <Multiple physical phenomena modeled in the same domain of analysis>

## Slide 7: Energy | Power Modeling
Energy (or power) is characterized w.r.t. architectural activities.
Architecture
Component
(e.g., Data Cache)
(Read Counts = 100)
(Write Counts = 50)
(Miss counts = 20)
Architecture Simulation
Power Modeling Tool
Architecture Configuration
Physical Configuration
X
X
X
(Per-read Energy = 10pJ)
(Per-write Energy = 15pJ)
(Tag-read Energy = 3pJ)
Estimation
= 1nJ
= 0.75nJ
=0.06nJ
(Total Energy = 1.81nJ)
/ (Period = 1ns) = 1.81W
Sampling Interval
Leakage Power = 0.95W
+
Component Power = 2.76W
Processor Power = ∑ (Component Power)
* Numbers are randomly chosen to show an example.

## Slide 8: Thermal Modeling
Temperature is characterized at the package-level w.r.t spatiotemporal distribution of power (i.e., power density).
Architectural components are placed on the processor die (floor-planning).
The package is represented with layers of thermal grid cells.
A grid cell model
L2 Cache
Core
* Floor-plan is arbitrarily drawn to show an example.

## Slide 9: Reliability (Hard Failure) Modeling
Failures | Description
Electro-migration (EM), λEM | Directional transport of electrons and metal atoms in interconnect wires causes degradation and failure.
Time dependent dielectric breakdown (TDDB), λTDDB | Wearout of gate oxide caused by continued application of electric field leads to short between gate and substrate.
Hot carrier injection (HCI), λHCI | Electrons with sufficient kinetic energy overcomes the barrier to gate oxide and cause degradation.
Bias temperature instability (NBTI/PBTI), λBTI | Gradual degradation causes threshold voltage shift and eventually timing errors.
Stress migration (SM), λSM | Differences in the expansion rates of metals cause mechanical stress.
Thermal cycling (TC), λTC | Temperature cycle accumulates fatigue to materials.
Failure Rate = ∑ (λFAILURE)
Mean-time-to-failure (MTTF)= 1/Failure Rate
The failure rate is a function of operating conditions (i.e., voltage, temperature).

## Slide 10: Architecture-Level Physical Modeling
Abstract Representation of Architecture-Physics Interactions

## Slide 11: STANDARDIZATION: <Compatible Integration of Different Modeling Tools>

## Slide 12: Data Definition
Different models use different types and units of data.
The EI defines the modeled physical data.
// Basic Units
typedef uint64_t Count;
typedef double Meter;
typedef double Hertz;
typedef double Volt;
typedef double Kelvin;
typedef double Watt;
typedef double Joule;
typedef double Unitless;
typedef double Second;
// Activity Counters
class counter_t {
Count switching;
Count read;
Count write;
Count read_tag;
Count write_tag;
Count search;
void clear();
};
// Energy
class energy_t {
Joule total;
Joule dynamic;
Joule leakage;
void clear();
Joule get_total();
};
// Power
class energy_t {
Watt total;
Watt dynamic;
Watt leakage;
void clear();
Watt get_total();
};
power_t operator*(const energy_t &e, const Hertz &f);
power_t operator/(const energy_t &e, const Second &s);
// Dimension
class dimension_t {
Index layer_index;
char layer_name[LEN];
Meter left, bottom;
Meter width, height;
MeterSquare area;
void clear();
MeterSquare get_area();
};
// Grid
template <typename T>
class grid_t {
unsigned x, y, z;
unsigned count;
std::vector<T> element;
T& operator[](unsigned i)
...
};

## Slide 13: Integration of Modeling Tools (1)
Tools that model the same physical phenomena are categorized into the same library.
Each library defines the functions to be provided by the models.
  Energy Library:
    It calculates runtime energy/power dissipation w.r.t. architectural activity
    It estimates TDP power and area (if possible).
    Integrated models: McPAT, IntSim, to be integrated: DSENT, DRAMsim
  Thermal Library:
    It calculates transient/steady-state temperature w.r.t. power inputs.
    It requires floor-planning for the functional dies.
    It provides different levels of thermal data; grid, block, or point temp.
    Integrated models: HotSpot, 3D-ICE, to be integrated: TSI, Microfluidics
  Reliability Library:
    It calculates failure rate w.r.t. operation conditions (i.e., voltage, temp).
    Integrated model: Hard Failure

## Slide 14: Integration of Modeling Tools (2)
// Base Library Class
class model_library_t {
virtual ~model_library_t();
virtual bool update_library_variable(int Type, void *Value, bool IsLibraryVariable)=0;
virtual void initialize()=0;
};
// Energy Library Class
class energy_library_t : public model_library_t {
virtual ~energy_library_t();
virtual unit_energy_t get_unit_energy()=0;
virtual power_t get_tdp_power(Kelvin MaxTemperature)=0;
virtual power_t get_runtime_power(Second Time, Second Period, Counter_t Counter)=0;
virtual MeterSquare get_area()=0;
};
// Thermal Library Class
class thermal_library_t : public model_library_t {
virtual ~thermal_library_t();
virtual void calculate_temperature(Second Time, Second Period)=0;
virtual grid_t<Kelvin> get_thermal_grid()=0;
virtual Kelvin get_partition_temperature(Comp_ID ComponentID, int MappingType)=0;
virtual Kelvin get_point_temperature(Meter X, Meter Y, Index Layer)=0;
virtual void push_partition_power(Comp_ID ComponentID, power_t PartitionPower)=0;
virtual void add_pseudo_partition(std::string ComponentName, Comp_ID ComponentID)=0;
...
};

## Slide 15: Integration of Modeling Tools – Example
// Example: Integration of HotSpot
#include <HotSpot header files>
class thermallib_hotspot : public thermal_library_t {
~thermalib_hotspot();
void initialize() {
/* DEFINE A METHOD TO CREATE AND INITIALIZE HOTSPOT DATA STRUCTURES AND VARIABLES */
}
void update_library_variable(int Type, void *Value, bool IsLibraryVariable) {
/* DEFINE A METHOD TO DYNAMICALLY UPDATE HOTSPOT DATA STRUCTURES AND VARIABLES */
}
void calculate_temperature(Second Time, Second Period) {
/* DEFINE A METHOD TO ACCESS HOTSPOT DATA STRUCTURES AND CALCULATE TEMPERATURE */
}
void push_partition_power(Comp_ID ComponentID, power_t PartitionPower) {
/* UPDATE THE PARTITION (i.e., FLOOOR-PLAN) POWER FOR THE NEXT TEMP. CALCULATION */
}
Kelvin get_partition_temperature(Comp_ID ComponentID, int MappingType) {
/* RETRIEVE THE PARTITION (i.e., FLOOR-PLAN) TEMP. AFTER calculate_temperature(); */
}
...
};
Each integrated tool becomes a subclass of one of the model libraries.

## Slide 16: CONFIGURABLE INTERFACE: <A method to represent the different levels of processor components – from processor package to microarchitecture units>

## Slide 17: Abstract Representation of Processor Hierarchy
How can we flexibly mix and match models, microarchitecture components, and physical geometry?

## Slide 18: Processor Representation (1)

## Slide 19: Processor Representation (2)
Different physical phenomena are characterized and different levels of processor components.
The EI is comprised of pseudo components that can represent any processor components
  A pseudo component can represent a package, die, core, floor-plan block, etc.
  A pseudo component can be associated with an integrated modeling tool to characterize a physical phenomenon.
// Pseudo Component
class pseudo_component_t {
pseudo_component_t(Comp_ID ID, libEI::energy_introspector_t *EI, std::string Name,
libconfig::Setting *ConfigSetting, bool IsRemote);
Comp_ID id; // Integer ID
int rank; // MPI Rank (for parallel simulation)
std::string name; // String name
model_library_t *model_library; // Associated library tool
queue_t queue; // Data queue that stores computed results or shared data
libEI::energy_introspector_t *energy_introspector; // Pointer to main interface
libconfig::Setting *setting; // libconfig setting for this pseudo component
libEI::pseudo_component_t *superset; // A parent component in the processor hierarchy
std::vector<libEI::pseudo_component_t*> subset; // Child components
...
};

## Slide 20: DATA SYNCHRONIZATION: <Time synchronization and data sharing between library models>

## Slide 21: Data Synchronization (1)
for(all components)
EI->calculate_power(ComponentID,Time,Period,Counter,/*IsTDP*/false);
EI->calculate_temperature(PackageID,Time,Period,/*PowerSync*/true);
for(all components)
EI->calculate_power(ComponentID,Time,Period,Counter,/*IsTDP*/false);
EI->synchronize_data(packageID,Time,Period,EI_DATA_POWER); // Sync Power
EI->calculate_temperature(PackageID,Time,Period,/*PowerSync*/false);
Or, alternatively
The EI provides handles data synchronization across pseudo components.
Different data types have different synchronization method:
  Power, Area: added up from the bottom of the pseudo component tree.
  Temperature, Voltage, Clock Freq: applied identically to sub-components.

## Slide 22: Data Synchronization (2)
Pseudo Component
Data Queue
Pseudo Component
Data Queue
Pseudo Component
Data Queue
Pseudo Component
Data Queue
Pseudo Component
Data Queue
Pseudo Component
Data Queue
synchronize_data(EI_DATA_POWER);
∑ (sub-component Power);
∑ (sub-component Power);
Queue Error Detection:
Time discontinuous
Time outorder
Time overlap
Time invalid
Data duplicated
Data invalid
Data type invalid
Invalid pseudo component

## Slide 23: Data Manipulation
Each pseudo component includes data queues to store computed results or shared data.
Data are of discrete time, and thus associated with time, period information.
  Closed Queue:
    This queue type is used for periodically calculated and sampled data such as power, temperature, etc.
    Data are continuous to the left; valid interval = (time-period, time]
  Open Queue: This queue type is used for aperiodically controlled data such as voltage, clock frequency, etc.
    Data are continuous to the right; valid interval = [time, unknown)
The insertion of data triggers the callback function of the library model (if any) to update dependent variables and states.
Simulation Progress
Time = 0.1sec
Period = 0.1sec
Time = 0.2sec
Period = 0.1sec
Time = 0.3sec
Period = 0.1sec
Sampling & Calculation

## Slide 24: Data Queue Structure
Each pseudo component includes data queues to store computed results or shared data.
// Base Queue
class base_queue_t {
virtual ~base_queue_t();
void reset();
int get_error();
unsigned size; // Queue length
int error; // Error code
};
// Individual Data Queue
template <typename T>
class data_queue_t : public base_queue_t{
~data_queue_t();
void reset();
void push(Second Time, Second Period, T Data);
void overwrite(Second T, Second P, T D);
T pull(Second T, Second P);
int queue_type; // Open / Close Queue
int data_type; // Data Type
std::map<data_time_t,T> queue;
};
// Pseudo Component Data Queue
Class queue_t {
~data_queue_t();
template <typename T>
void create(unsigned QueueLength,
int DataType, int QueueType);
template <typename T>
void push_back(Second Time, Second Period,
int DataType, T Data);
template <typename T>
void overwrite(Second Time, Second Period,
int DataType, T Data);
template <typename T>
T get(Second Time, Second Period,
int DataType);
void register_callback(model_library_t *Lib,
bool(model_library_t::*update_library_variable)
(int,void*,bool));
void callback(int DataType, void *Data);
int get_error();
void reset();
std::map<int,base_queue_t*> queue;
};

## Slide 25: INPUT CONFIG & USER INTERFACE: <EI Configuration and User API>
Package
(thermal)
Core0
(Reliability)
Core1
(Reliability)
Core2
(Reliability)
Core3
(Reliability)
Shared L2
(Energy)
Inst Cache
(Energy)
BTB
(Energy)
Inst Decoder
(Energy)
…
(Energy)
ALU
(Energy)
LD/STQ
(Energy)
* Within () shows the modeled library at each pseudo component.
Thermal Library = 3D-ICE
Reliability Library = Hard Failures
Energy Library = McPAT

## Slide 26: Input Configuration
The EI uses the libconfig to parse the input file.
// Example
component: {
package: {// package
library: {
model = “3d-ice”;
ambient_temperature = 300.0;
grid_rows = 100;
/* 3D-ICE PARAMETERS */
};
component: {
core0: {// package.core0
  library: {
  model = “none”;
  voltage = 0.8;
  clock_frequency = 2.0e9;
  /* COMMON PARAMETERS OF core0 */
  };
  component: {
  data_cache: {
  };
  };
}; // package.core0
};
}; // package
};
// Continued with core.data_cache
component: {
data_cache: {// package.core0.data_cache
library: {
model = “mcpat”;
energy_model = “array”;
energy_submodel = “cache”;
line_sz = 64;
assoc = 4;
/* MCPAT PARAMETERS */
/* NO NEED TO REDEFINE voltage */
};
}; // package.core.data_cache
inst_dec: {// package.core0.inst_dec
library: {
model = “mcpat”;
energy_model = “inst_decoder”;
x86 = true;
/* MCPAT PARAMETERS */
};
}; // package.core0.inst_dec
...
};

## Slide 27: User API Example (1)
The simulator creates the Energy Introspector.
Each manifold model has the pointer to the Energy Introspector.
// Example – Serial Simulation
/* MAIN FUNCTION: CREATE AND CONFIGURE THE ENERGY INTROSPECTOR */
energy_introspector_t *ei = new energy_introspector_t(“input.config”); // Create EI
ei->configure(); // Configure EI
...
/* CONNECT EI INTERFACE – SERIAL SIMULATION */
Core_t *core = Component :: GetComponent<core_t>(ManifoldCoreID);
core->connect_EI(ei);
core->set_sampling_interval(0.0001);
...
Manifold :: Run();
...

## Slide 28: User API Example (2)
The EI provides several API functions to use the models.
/* WITHIN A MANIFOLD MODEL */
Comp_ID package_id, core_id, data_cache_id;
...
/* IDs ARE REQUIRED FOR ALL COMPONENTS WHERE DATA ARE MONITORED */
counter_t data_cache_counter; // Data cache counter
...
/* COUNTERS ARE DEFINED FOR ALL COMPONENTS WHERE POWER IS CHARACTERIZED */
void core_t::connect_EI(energy_introspector_t *ei) {
energy_introspector = ei;
// Get the pseudo component ID of modeled processor components
package_id = energy_introspector->get_component_id(“package”);
assert(package_id != INVALID_COMP_ID);
...
}
void core_t::tick() {
if(NowTicks() % sampling_interval == 0) {
/* ARCHITECTURE SIMULATION IS PERFORMED, AND COUNTERS ARE COLLECTED FOR DATA CACHE */
energy_introspector->calculate_power(data_cache_id,time,period,data_cache_counter);
/* calculate_power() IS CALLED FOR ALL COMPONENTS WHERE POWER IS CHARACTERIZED */
energy_introspector->calculate_temperature(time,period,/*PowerSync?*/true);
int err; Kelvin core_temp; // Data are already sync’ed
err = energy_introspector->pull_data(core_id,time,period,EI_DATA_TEMPERATURE,&core_temp);
}
}

## Slide 29: DEMONSTRATION <Architecture-physics co-simulation via Manifold and Energy Introspector>
// Trace file from the simulation
time= 124.0 | core0
instantIPC= 0.997120 , avgIPC= 1.008513
power= 2.195946 W (dynamic= 1.299701 W, leakage= 0.896246 W, area= 5.28mm^2)
clk= 2.000 GHz, temp= 332.3, failure_rate= 1.934528e-11 (MTTF= 1.269645)
time= 124.0 | core1
instantIPC= 1.088155 , avgIPC= 1.089841
power= 2.325650 W (dynamic= 1.418857 W, leakage= 0.906793 W, area= 5.28mm^2)
clk= 2.000 GHz, temp= 335.9, failure_rate= 2.228109e-11 (MTTF= 1.102353)
time= 124.0 | core2
instantIPC= 1.372630 , avgIPC= 1.239406
power= 2.698654 W (dynamic= 1.791860 W, leakage= 0.906793 W, area= 5.28mm^2)
clk= 2.000 GHz, temp= 335.8, failure_rate= 2.189546e-11 (MTTF= 1.121768)
time= 124.0 | core3
instantIPC= 1.124560 , avgIPC= 1.050577
power= 2.361293 W (dynamic= 1.465048 W, leakage= 0.896246 W, area= 5.28mm^2)
clk= 2.000 GHz, temp= 333.0, failure_rate= 1.958338e-11 (MTTF= 1.254208)

## Slide 30: PARALLEL INTERFACE: <Parallel Simulation via MPI interface>
Manifold Process 1
Package
(thermal)
Core0
(Reliability)
Core1
(Reliability)
Core2
(Reliability)
Core3
(Reliability)
Shared L2
(Energy)
EI Process 1
EI Process 0
Core0
Core1
Core2
Core3
Shared L2
Manifold Process 0
Network
MPI Inter-communicator

## Slide 31: Parallel EI Configuration
The EI supports parallel simulation via the MPI interface.
The pseudo component hierarchy can be partitioned into multiple MPI processes.
// Example – Rank0
component: {
package: {// package
library: {
model = “3d-ice”;
ambient_temperature = 300.0;
grid_rows = 100;
/* 3D-ICE PARAMETERS */
};
component: {
core0: {// package.core0
  remote = true;
}; // package.core0
core1: {// package.core1
  remote = true;
}; // package.core1
core2: {// package.core2
  model = “none”;
}; // package.core2
...
};
}; // package
};
// Example – Rank1
component: {
package: {// package
library: {
remote = true;
};
component: {
core0: {// package.core
  library: {
  model = “none”;
  voltage = 0.8;
  clock_frequency = 2.0e9;
};
...
}; // package.core
};
}; // package
};

## Slide 32: Parallel API Example (1)
The MPI process creates the Energy Introspector.
// Example – Parallel Simulation
/* MAIN FUNCTION: CREATE AND SPLIT THE MPI COMMUNICATOR FOR MANIFOLD AND EI */
MPI_Comm INTER_COMM, LOCAL_COMM;
MPI_Comm_split(MPI_COMM_WORLD,(MyRank<Manifold_NPs),Rank,&LOCAL_COMM);
MPI_Intercomm_create(LOCAL_COMM,0,MPI_COMM_WORLD,MyRank<Manifold_NPs?
Manifold_NPs:0,1234,&INTER_COMM);
/* CREATE AND CONFIGURE THE ENERGY INTROSPECTOR */
energy_introspector_t *ei = new energy_introspector_t(“input-rank0.config”,
INTER_COMM,LOCAL_COMM);
ei->configure(); // Configure EI
...
Manifold :: Init(argc,argv,&LOCAL_COMM); // Manifold runs within its MPI communicator
...
/* INSTANTIATE EI CLIENT – PARALLEL SIMULATION */
Core_t *core = Component :: GetComponent<core_t>(ManifoldCoreID);
core->connect_EI(&INTER_COMM, Rank);
core->set_sampling_interval(0.0001);
...
Manifold :: Run();
...

## Slide 33: Parallel API Example (2)
The EI client is used to communicate over MPI processes.
/* WITHIN A MANIFOLD MODEL */
void core_t::connect_EI(MPI_Comm *InterComm, int EIRank);
// Create EI client interface
EI_client_t *EI_client = new EI_client(InterComm,EIRank);
// Get the pseudo component ID of modeled processor components
package_id = EI_client->get_component_id(“package”);
assert(package_id != INVALID_COMP_ID);
...
}
void core_t::tick() {
if(NowTicks() % sampling_interval == 0) {
/* ARCHITECTURE SIMULATION IS PERFORMED, AND COUNTERS ARE COLLECTED FOR DATA CACHE */
EI_client->calculate_power(data_cache_id,time,period,data_cache_counter);
/* calculate_power() IS CALLED FOR ALL COMPONENTS WHERE POWER IS CHARACTERIZED */
EI_client->calculate_temperature(time,period,/*PowerSync?*/true);
Kelvin core_temp; power_t core_power; // Data are already sync’ed
int err = EI_client->pull_data(core_id,time,period,EI_DATA_POWER,&core_power);
err = EI_client->pull_data(core_id,time,period,EI_DATA_TEMPERATURE,&core_temp);
}
}

## Slide 34: EI: Summary
The Energy Introspector is an enabler for architecture-physics exploration.
Any new models can be incorporated into the interface, and we plan to add more models.
For an access to the latest EI:
svn co https://svn.ece.gatech.edu/repos/Manifold/trunk/code/models/energy_introspector/

## Slide 35: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators