## Slide 1: What can Manifold Enable?
Manifold enables cross-disciplinary evaluations
Applications  Power  Thermal  Cooling
Multi-scale simulation  cycle-level to functional
Tradeoff studies
Performance
Reliability
Energy/Power
www.commons.wikimedia.org
imaging1.com
Large Graphs

## Slide 2: Some Example Simulators
Power capping studies
Reliability studies
Workload  Cooling interaction

## Slide 3: Power Capping: Simulation Model
Power Targets
Controller gain is adjusted every 5 ms
Each core has its own core and power budget – two OOO and two IO cores.

## Slide 4: Power Capping Controller
High fixed-gain controller over-reacts to high power cores, whereas low fixed-gain control is slow to react to low power cores.
N. Almoosa, W. Song, Y. Wardi, and S. Yalamanchili, “A Power Capping Controller for Multicore Processors,” American Control Conf., June 2012.
New set point

## Slide 5: Throughput Regulation: Adaptive
High fixed-gain controller over-reacts to high power cores, whereas low fixed-gain control is slow to react to low power cores.
N. Almoosa, W. Song, Y. Wardi, and S. Yalamanchili, “Throughput Regulation on Multicore Processors via IPA,” 2012 IEEE 51st Annual Conference on Decision and Control (CDC)

## Slide 6: Adaptation to Aging and Reliability
64-core asymmetric processor floor plan
Failure probability comparison between per-core race-to-idle executions (left) and continuous low-voltage executions (right)
Transient race-to-idle executions vs. continuous executions
LVF: Low Voltage Frequency
HVF: High Voltage Frequency
NVF: Nominal Voltage Frequency

## Slide 7: Workload-Cooling Interaction
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
Nehalem-like, OoO cores;
3GHz, 1.0V, max temp 100◦C
DL1: 128KB, 4096 sets, 64B
IL1: 32KB, 256 sets, 32B, 4 cycles;
L2 & Network Cache Layer:
L2 (per core): 2MB, 4096 sets, 128B, 35 cycles;
DRAM: 1GB, 50ns access time (for performance model)
Ambient:
Temperature: 300K
Thermal Grids: 50x50
Sampling Period: 1us
Steady-State Analysis
2.1mm x 2.1mm
8.4mm x 8.4mm
16 symmetric cores
CORE DIE
MICROFLUIDICS
SRAM
Coolant/Configuration | A | B | C
Flow rate (ml/min) | 7 | 42 | 84
Top Heat Coeff (W/um2-K) | 2.05e-8 | 5.71e-8 | 8.01e-8
Bot. Heat Coeff (W/um2-K) | 1.69e-8 | 4.72e-8 | 6.63e-8

## Slide 8: Impact of Flow Rate & Workload on Energy Efficiency
Chart: nJ/inst
| barnes | canneals | fft | ocean-c | radix
A | 2.47 | 2.37 | 2.24 | 2.38 | 2.63
B | 2.32 | 2.21 | 2.15 | 2.16 | 2.26
C | 2.22 | 2.12 | 2.13 | 2.14 | 2.17
Chart: MIPS/W
| barnes | canneals | fft | ocean-c | radix
A | 404.8583 | 421.9409 | 446.4286 | 420.1681 | 380.2281
B | 431.0345 | 452.4887 | 465.1163 | 462.963 | 442.4779
C | 450.4505 | 471.6981 | 469.4836 | 467.2897 | 460.8295
Memory bound applications benefit more than computation bound applications
Overall energy improvement
  4.9%-17.1% over 12X increase in flow rate
  4.0%-14.1% over 6X increase in flow rate
Does not include pumping power

## Slide 9: 3D Stacked ICs Structure Model
3D stacked ICs structure
Simplified structure
Conduction FE model and temperature results
heff=562.4 W/m2*K
Effective heat transfer coefficient is obtained by FE model on the left:
Z. Wan et. al., IEEE Therminic 2013, Berlin, 25. -27. Septemeber 2013 (accepted)

## Slide 10: Case Study with Different Microgap Configurations
Microgap configurations
Configuration 1: One microgap
Configuration 2: Two microgaps
Temperature results: One microgap, logic tier at bottom and memory tier on the top
Pump power:0.03 W | Configuration |  |  | Tmax,logic (℃) | Tmax,memory (℃)
 | Micro-gap | Top | Bottom |  | 
Case 1 | 1 | M | L | 93.1 | 82.2
Case 2 | 1 | L | M | 114.9 | 77.1
Case 3 | 2 | M | L | 87.7 | 54.8
Case 4 | 2 | L | M | 72.7 | 58.3
Logic tier
Memory tier
Results for different cases

## Slide 11: Summary
Not to provide a simulator, but
Composable simulation infrastructure for constructing multicore simulators, and
Provide base library of components to build useful simulators
Novel Cooling Technology
Thermal Field Modeling
Power Distr. Network
Power Management
μarchitecture
Algorithms
Microarchitecture
and Workload Execution
Power Dissipation
Thermal Coupling
and Cooling
Degradation
and Recovery
www.manifold.gatech.edu